## Slide 1: A novel injection scheme using R.F. manipulation for SOLEIL upgrade
M.-A. Tordeux on behalf of Accelerators and Engineering Division

## Slide 2
Upgrade project
Top-Up injection process
Manipulation in longitudinal plane
Analogy between transverse and longitudinal planes
Summary

## Slide 3: Upgrade project
Constraints among a long list:
Reuse of the existing tunnel and its radiation shielding wall  machine with same length of 350 m and specific geometry to maintain the existing insertion device source points as much as possible.
Preserve a current of 500 mA in multibunch operation, preserve time structure and time resolved operations with top-up injection.
Future upgrade of SOLEIL 
Reduce the horizontal emittance below 100 pm.rad
in order to maximize the intensity of coherent photon flux arriving at the beamlines, especially in the soft tender X-rays range up to 3 keV.

## Slide 4: Top-Up injection process (transverse plane)
x= 4 nm.rad
Present SOLEIL lattice
1/8 ring
Off axis injection of the Booster beam
Simulated Dynamic Aperture without error
Injection kickers
Injected beam
Stored beam
Large betatron oscillation
Off axis injection

## Slide 5: Top-Up injection process (transverse plane)
x= 72 pm.rad
1/8 ring
Baseline lattice for Upgrade:
7BA structure
Forget OFF axis injection!
Simulated Dynamic Aperture without error
Pinhole!

## Slide 6: Top-Up injection process (transverse plane)
x= 72 pm.rad
1/8 ring
Try ON axis injection
Simulated Dynamic Aperture without error
Pinhole!
But standard on-axis injection scheme (swap-out) requires ultra-fast kickers that are far from feasibility in SOLEIL case (352 MHz).
Baseline lattice for Upgrade:
7BA structure

## Slide 7: Top-Up injection process (transverse plane)
x= 72 pm.rad
1/8 ring
MIK = Multipole injection kicker
Injected beam
Stored beam
Chromatic axis for a beam which is shifted in energy
This is an ON (chromatic)-axis injection!
Baseline lattice for Upgrade:
7BA structure
Simulated Dynamic Aperture without error
DA ( = + 6%)
Simulated Dynamic Aperture without error

## Slide 8: Top-Up injection process (transverse plane)
MIK = Multipole injection kicker
Injected beam
Stored beam
Chromatic axis for a beam which is shifted in energy
This is an ON (chromatic)-axis injection!
Field profile for MIK
Unperturbed
stored beam
Chromatic axis for 6% energy offset
The MIK is a magnetic device with zero field on axis (no perturbation of the stored beam), and a field off axis that will kick the injected beam on the chromatic axis.
Device already installed on MAXIV Lab., soon on SOLEIL (collaboration SOLEIL, MAXIV Lab.).

## Slide 9: Manipulation in longitudinal plane
How to capture a particle which is shifted in energy (« off-momentum »)?
Natural trajectory
Particle is lost!
Origin of phase corresponding to s
Injection
6% energy offset

## Slide 10: Manipulation in longitudinal plane
How to capture a particle which is shifted in energy (« off-momentum »)?
Cf. M. Aiba et al., Longitudinal injection scheme using short pulse kicker for small aperture electron storage rings,
Phys. Rev. ST Accel. Beams 18, 020701 (2015).
Idea from SLS group: use the natural golf club shape of the longitudinal plane to inject and store an off-momentum beam, in top-up mode.
Injection of an off-momentum beam at phase - 
Natural damping into the stored beam

## Slide 11: Manipulation in longitudinal plane
How to capture a particle which is shifted in energy (« off-momentum »)?
Applied to SOLEIL Upgrade (baseline lattice with 3rd harmonic cavity)
Origin of phase corresponding to s

## Slide 12: Manipulation in longitudinal plane
How to capture a particle which is shifted in energy (« off-momentum »)?
5 ps
2 10-3
Injected bunch length and energy spread acceptance uncompatible with Booster performances
Energy offset too low to spread enough the chromatic orbit and allow the use of a MIK
Applied to SOLEIL Upgrade
Origin of phase corresponding to s

## Slide 13: Manipulation in longitudinal plane
Natural trajectory
Particle is lost!
Origin of phase corresponding to s
How to capture a particle which is shifted in energy (« off-momentum »)?
Keep the idea of injection at phase - 

## Slide 14: Manipulation in longitudinal plane
Natural trajectory
Forced trajectory: Particle is captured into the longitudinal bucket
+ Longitudinal kick
How to capture a particle which is shifted in energy (« off-momentum »)?
Origin of phase corresponding to s

## Slide 15: Manipulation in longitudinal plane
Injected beam
i = -  and i = + 6 %
Plot every 50 turns
+ Longitudinal kick
Case of a realistic beam from a Booster
Origin of phase corresponding to s

## Slide 16: Manipulation in longitudinal plane
The longitudinal kick is produced by an additional RF pulse, during the time of injection.
Procedure:
  Switch on VRF add before beam is injected @ phase -
  Switch off when beam reaches s , after ~200 turns
Requirements:
Do not perturb the stored beam
Main 352 MHz RF pulse and its 3rd harmonic for operation
Vmain = 0.9 MV
U0 = 310 keV/turn
+ additional pulses during injection:
Vad 352 MHz = 1.4 MV + shifted by s
Vad 3rd = Vadd /3
Additional
transient
RF pulse
Plot every 50 turns
Injected beam
Unperturbed
stored beam

## Slide 17: Manipulation in longitudinal plane
Switch on / off takes into account the loaded quality factor QL of cavities:
One must consider:
  How to get similar L for 3rd HC compared to main RF
  The phase control of main RF during voltage change
Injection time
Start to switch off, lets say 75 µs before time of beam reaching s
75 µs
175 µs
Worse case of supraconducting RF: QL = 105 , L = 90 µs
 still compatible with beam dynamics.
0.9 MV
Start to switch off
Total VRF add seen by the ‘central’ particle during injection process
Main RF:
V = +1.4 MV dephased by s
@ 3 Hz as a first approach
Injected beam

## Slide 18: Analogy between transverse and longitudinal planes
Field profile for Transverse NLK (MIK)
Voltage profile for Longitudinal NLK (RF)
A beam with energy offset is put on chromatic axis with a transverse Non Linear Kicker (MIK) …
… and launched from an offset phase (- ), its energy is damped thanks to a longitudinal Non Linear Kicker (transient RF pulse - main and harmonic).
Additional
transient
RF pulse
Injected beam
Unperturbed
stored beam
Unperturbed
stored beam
Injected beam

## Slide 19: Summary
The use of a Transverse NLK (MIK) allows to inject an off-momentum beam ON (chromatic) AXIS. Unlike swap-out injection method, this doesn’t require very fast kicker, but a ‘slow’ MIK.
Then the beam is captured in the longitudinal plane thanks to a Longitudinal NLK. No short injected beam is needed. Damping process in longitudinal plane is accelerated.
Impact of errors are under investigation (Injector, Storage Ring magnets, R.F.), together with simulation on different lattices.
R.F. tests are under way (see presentation P. Marchand)
Issue on Harmonic Cavity: is there any possibility not to modulate its voltage during injection, without any impact on stored beam?