## Slide 1
Compact linear accelerator FLUTE: status update
Anton Malygin, A. Bernhard, A. Böhm, E. Bründermann, S. Funkner, B. Härer, S. Marsching, W. Mexner, M. J. Nasse, G. Niehues, R. Ruprecht, T. Schmelzer, M. Schuh, M. Schwarz, N. Smale, P. Wesolowski, M. Yan, A.-S. Müller

## Slide 2
Main goals for FLUTE
  Test facility for accelerator physics
  Compare CSR in simulation and experiment
  Experiments with THz radiation
  Test bench for new beam diagnostics
R&D topics
  Development of single-shot fs diagnostics
  Synchronization on a femtosecond level
  Systematic bunch compression and THz generation studies
FLUTE: Ferninfrarot Linac- Und Test-Experiment
Final electron energy | ~ 41 | MeV
Electron bunch charge | 1 pC - 3 | nC
Electron bunch length | 1 - 300 | fs
Pulse repetition rate | 10 | Hz
THz E-Field strength | up to 1.2 | GV/m

## Slide 3: FLUTE: Layout
A – Experimental hall:
1 – Klystron with auxiliaries
2 – RF photo-injector gun
3 – Linac 4 – Bunch compressor
B – Laser clean room
C – Airlock
D – THz measurement room
E – Control room
F – Entrance area

## Slide 4: FLUTE: Layout & implementation
Energy | 7 MeV
Bunch charge | 1 pC-3 nC
Beam size | 0.4-4.5 mm
Bunch length | 500 fs-2.5 ps
Energy spread | 0.14-0.8 %
𝝺 (laser) | 266 nm
Spot size | 0.5-2.5 mm
Pulse length | 500 fs-2 ps
Energy | 41 MeV
Bunch charge | 1 pC-3 nC
Beam size | 0.4-4.5 mm
Bunch length | 500 fs-2.5 ps
Energy spread | 0.24-1.8 %
Energy | 41 MeV
Bunch charge | 1 pC - 3 nC
Beam size | 40µm - 3 mm
Bunch length | few fs - 500 fs
Energy spread | 0.24 -1.8 %
7-MeV section
41-MeV section
Buncher and THz section

## Slide 5: RF system configuration

## Slide 6: Beam diagnostics

## Slide 7: RF photo-injector configuration:
RF photo-injector parameters |  | 
Frequency | 2.998 | GHz
Cells | 2.5 | 
Peak E-field | 100 | MV/m
Peak power | 20 | MW
Output energy | 7 | MeV
Maximum charge extracted from cathode per short:
Cu cathode up to 700 pC (assembled)
Cs2Te up to 3 nC (planned)
Drawing taken from: R. Bossart, et. al. “A 3 GHz photoelectron gun for high beam intensity”, Nuclear Instruments and Methods in Physics Research, A 375 (1996) ABS 7 – ABS 8.

## Slide 8: RF photo-injector commissioning results:
Input power from the klystron (red line – left axis) and normalised signal from the RF probe pick-up (first cell) (green line – right axis).
Signal from RF probe pick ups from three cells.
Red – first half-cell, Green- second cell, Blue – third cell.
Input power into RF gun – 4 MW
Electron beam energy – 2 MeV
Drawing taken from: R. Bossart, et. al. “A 3 GHz photoelectron gun for high beam intensity”, Nuclear Instruments and Methods in Physics Research, A 375 (1996) ABS 7 – ABS 8.

## Slide 9: First electron beam:
YAG screen monitor
Typical Faraday cup output (connected via a coax cable to a 1 MΩ terminated oscilloscope). Orange curve shows the histogram of the Faraday cup signal.
Typical ICT signal. ICT trigger (green), ICT analog output (yellow), ICT capture and hold signal of the yellow trace (blue), histogram of the capture and hold signal (pink).
Faraday cup signal
Histogram
Dark current
Noise
ICT signal
Histogram
Noise
Laser ON

## Slide 10: Split ring resonator experiment at FLUTE
RF gun
Quadrupole
e-beam
~3 m
Solenoid
SRR chamber
Dipole
magnet
Steerer
Profile
monitor

## Slide 11: Principle of SRR diagnostics
„Split ring resonator based THz-driven electron streak camera featuring femtosecond resolution“
    J. Fabiańska, G. Kassier, T. Feurer, Sci. Rep. 4, 5645 (2014)
    M. Yan et al., TUPG56, IBIC 2016, Barcelona, Spain.
THz-range => high frequency f
  LiNbO3 crystal => 35 fs pulse at 800 nm (FLUTE laser) converted to THz pulse
Field enhancement in SRR gap => large “kick” voltage V
  Enhancement factor ~100 (at 0.3 THz)
THz
pulse
UV
pulse
E(t) in SRR gap
electric field
fs laser
<2 ps
LiNbO3
3´n
n

## Slide 12: Laser system modifications:
New optical table has been installed next to the beam diagnostics section.
RF injector
Compressor
SRR signal
Compressor
Cathode signal
Pulse picker
THG
SRR chamber
Laser pulse

## Slide 13: RF system commissioning
Klystron
Power splitter
Phase shifter
Circulator
RF injector
Linac
Problems and solutions:
Leaks (SF6 gas) were found in the power splitter and the phase shifter – have been fixed
Circulator showed high insertion loss of 1.5 dB instead of 0.2 dB – new circulator was ordered expected delivery April 2019.
RF components and RF power:
Power splitter – 45 MW (RF power)
Phase shifter – 25 MW
New circulator – 20 MW
RF injector – 20 MW

## Slide 14: Bunch compessor
Dipole
Quadrupole
Linac
Bunch compressor
Beam dump
THz line
Dipoles have been delivered, measurement of magnetic field distribution is in progress at KIT and compared to the specifications.
Quadrupoles are in production.

## Slide 15: Summary and Outlook
Assembly of the FLUTE RF injector (7 MeV) and associated diagnostics completed, conditioning ongoing – First electron beam measured
Conditioning results: RF power: 4 MW (limited by faulty circulator), Electron beam energy: 2 MeV, pulse length: 4.5 µs, repetition rate: 1 Hz has been reached
New circulator will be installed on April 2019. This will allow to continue RF conditioning of different RF components. RF–laser synchronization is in progress.
Dipoles for the bunch compressor have been delivered
Next steps: commissioning of the new circulator, power splitter, phase shifter and RF gun at full power, RF-laser synchronization, assembling Linac and the Linac RF distribution system, conditioning Linac. Optimizing the design and assembly of the bunch compressor.
Thank you for your attention!